## Slide 1
GUIDED BY PRESENTED BY
DR. SATHESH . M 1. JOHN DAVID RAYEN. E (VTU 23006)
Assistant Professor 2. AARTHY. B (VTU 22415)
3. PATTABI NEELAKANTA (VTU 22486)
Smart helmet with drunk driving prevention and rescue

## Slide 2: ABSTRACT
Motorcycle accidents are a leading cause of fatalities, often due to alcohol consumption and failure to wear helmets. To address this, we propose a Smart Helmet that incorporates alcohol detection and accident notification features to enhance rider safety. The helmet is equipped with an MQ-3 alcohol sensor that detects alcohol levels in the rider's breath. If the alcohol content exceeds a predefined threshold, the motorcycle ignition is automatically disabled, with the help of relay module which is installed to the bike’s ignition part preventing the rider from starting the vehicle. MPU6050 accelerometer detects sudden impacts, which are indicative of accidents. Once an accident is detected, a GSM module sends an alert with the rider’s GPS location to emergency contacts . The entire system is controlled by a microcontroller (ESP8266).This project aims to significantly reduce accidents caused by intoxicated riders, enhance emergency response efficiency and enforce helmet usage, ultimately promoting safer roads. Through the integration of sensor technology and IoT, this Smart Helmet offers a preventive and life-saving solution for motor riders.

## Slide 3: OBJECTIVE
Stop Drunk Driving : Detect alcohol in the rider’s breath using a sensor. If the alcohol level is too high, the bike won’t start, helping prevent drunk driving.
Accident Detection : Sense accidents in real-time using motion sensors that can detect sudden jerks, falls, or collisions.
Send Emergency Alerts : If an accident happens, the helmet will automatically send an SOS message with the rider’s location to emergency contacts, so help can reach quickly.
Easy Wireless Communication : Use WIFI for smooth, low-power wireless communication between the helmet and the bike or other connected devices.
Promote Safe Riding : Encourage responsible riding habits by using smart technology to protect riders.

## Slide 4: INTRODUCTION
The Smart Helmet with Integrated Alcohol Detection and Accident Notification is a smart safety device designed to make two-wheeler riding safer, especially on Indian roads where accidents are a major concern. This helmet comes with an alcohol detection sensor (MQ-3) that checks the rider’s breath. If alcohol levels are above the safe limit, the system won’t allow the bike to start, helping to prevent drunk driving . Along with this, the helmet has an accident detection system using sensor. The MPU-6050 (gyroscope / accelerometer) to sense sudden impacts or falls. In case of an accident, It sends an SOS alert with the rider’s location using GPS module to emergency contacts, ensuring quick help reaches the spot . The helmet uses WIFI transmission platform to smooth, wireless communication between the helmet and the bike . The SMS is send through the Twilio number provided to the ESP8622 microcontroller. By combining embedded systems with IoT, this Smart Helmet aims to promote responsible riding habits, reduce road accidents, and ensure faster emergency responses. It’s a small step towards making our roads safer for everyone.

## Slide 5: BLOCK DIAGRAM
MQ3 SENSOR
ESP8266
MPU6050
POWER SUPPLY
ESP8266
RELAY MODULE
GPS MODULE
TWILIO
POWER SUPPLY
TRANSMITTER PART
RECEIVER PART

## Slide 6: Methodology
Design and Setup :
The helmet is fitted with an alcohol sensor (MQ-3), an accident detection sensor (MPU-6050), a GPS module and a microcontroller .All the components are neatly placed inside the helmet and connected to the bike’s ignition system.
Alcohol Detection :
When the rider wears the helmet, the alcohol sensor checks their breath . If alcohol is detected above the safe limit, the system automatically blocks the bike from starting using a relay module . This helps to prevent drunk driving.
Accident Detection :
The helmet constantly monitors the rider’s movements through MPU6050 . If it detects a sudden impact, fall, or unusual motion, it considers it an accident.

## Slide 7
Emergency Alerts :
In case of an accident, the helmet sends an SOS message with the rider’s location to emergency contacts using a Twilio account provided and location is detected by a GPS module .
Testing and Final Setup :
The system is tested in different situations to make sure the alcohol detection, accident alerts, and communication work perfectly.
Methodology

## Slide 8: Hardware USED
Microcontroller : ESP32 or ESP8266 (For processing data). The function of the components is monitored and programmed based on our code or instructions.
Alcohol Sensor : MQ-3 (For detecting alcohol in the rider’s breath). MPU-6050 (For accident detection through motion and impact sensing). It acts as both accelerometer and gyroscope.
GSM Module : NEO-6M (for tracking the exact location during an accident).
Power Supply Rechargeable Battery: Li-ion or Li-Po battery with a proper charging module .Voltage Regulator:LM7805 (to maintain stable voltage for sensitive components)(optional) .
Relay Module : To control the ignition system (preventing the bike from starting if the rider is intoxicated).
Wires & Connectors : For linking sensors and modules .

## Slide 9: Software Used
Embedded Programming : Arduino IDE , A platform used to program the microcontrollers (ESP8266) and help to feed it into the microcontroller and can also be used to verify the code.
WIFI Communication : A WIFI connection is provided for the transmission of data between the helmet (Transmitter part) and bike (ignition part) .
Microcontroller Firm ware C++ : The most common languages for embedded systems and IOT related projects.
Proteus / LT Spice : It is a online platform used for microcontroller and circuit simulation process where it gives a detailed idea of the project .
Twilio website : A online platform used to send SMS to the emergency contacts with the provided number and the location of the accident can be transmitted.

## Slide 10: Timeline Plan
Sl. No. | WEEK no. | DESCRIPTION
1 | WEEK 1 | Research and finalize the requirements for the project.
2 | WEEK 2 | Literature survey , study of microcontroller , GSM module and budget estimation .
3 | WEEK 3 | System design, designing of the block diagram and circuit logic .
4 | WEEK 4 | Optimize the ESP8266 code to handle sensor inputs and SMS alerts..
5 | WEEK 5 | Testing individual components debugging hardware and software.
6 | WEEK 6 | Analyze the performance of the hardware components under different conditions.
7 | WEEK 7 | Analyze the simulation result and discuss finding and limitations.
8 | WEEK 8 | Completion of the prototype with all the requirements.
9 | WEEK 9 | Write the final research report methodology, results and conclusions.
10 | WEEK 10 | Prepare a manuscript based on the project and submit to relevant journal.

## Slide 11: References
K. Ramesh , "Smart Helmet for Alcohol Detection and Accident Prevention," International Journal of Engineering Research & Technology (IJERT), 2021.
A. Kumar, et al., "A Zigbee-Based Alcohol Detection and Accident Notification System," International Journal of Advanced Research in Electronics and Communication Engineering (IJARECE), 2020.
S. Gupta, et al., "IoT-Based Smart Helmet for Accident Detection and Prevention," IEEE Xplore, 2022.
R. K. Sharma, G. Kumar, Bestley Joe "Smart Helmet Prototype for Safety Riding and Alcohol Detection” IEEE Bangalore Humanitarian Technology Conference (B-HTC), 2020.

## Slide 12: Thank you